## Slide 1: GM PAN ASM-UPR OIL Technical Review
DaeYong Industry Co.
DUNS 687885681
Oct 10, 2024
Part Name : PAN ASM-UPR OIL
Part No. : 25206258(ASSEMBLY)
BGH00954(MCHG)
RFQ No. : 601088175

## Slide 2: Contents
Contents
Introductions
Company Overview
Quality Data
Manufacturing Plan
Technical Data
Testing & Validation Plan
Timing Plan
Engineering Design & Development
Supply Chain Plan (Logistics, Packaging)
Commercial review
PAN ASM-UPR OIL
25206258(ASSEMBLY)

## Slide 3: Parts Quoted
Date of Tech Review : Oct. 10. 2024
Supplier Name : DaeYong Industry Co.
Proposed Mfg. Site : MTV & Sihwa Plant, S.Korea
DUNS NO. : 687885681
RFQ NO. : 601088175
Part Number & Design Level : bgh28391.drawing001.001016
2D Drawing (MCHG : R001)
25206258.drawing001.001013
2D Drawing (ASSEMBLY : R001)
Appendix B Date & Revision: 03. June. 2024 / Rev.004
PAN ASM-UPR OIL
25206258(ASSEMBLY)
PAN-OIL
BGH00954(MCHG)

## Slide 4
List of Tech Review participants
Title | Name | Phone Number | E-Mail Address
Engineering General Manager | N.K. Ryu | +82 31 500 2843 | nkryu@daeyong.co.kr
Technical Sales Sr. Manager | Chris Park | +82 31 500 2839 | kspark@daeyong.co.kr
Engineering Sr. Manager | S.B. Lee | +82 31 500 2850 | sblee@daeyong.co.kr
Engineering Manager | H.S. Kim | +82 31 500 2848 | hskim@daeyong.co.kr
Technical Sales Manager | John Kim | +82 31 500 2858 | twkim2@daeyong.co.kr
Account Manager | Matthew Kern | +1 248 227 5511 | mkern@dyc-usa.com
Sales Engineer | Jayden Chun | +1 917 806 3636 | dchun@gkasales.com
Ⅰ. Introductions

## Slide 5: Ⅱ. Company Overview - Corporate structure & divisions
TOP MANAGEMENT
PLANT DIRECTOR
FUNCTIONAL
GROUP
OPERATIONAL
TEAM
CEO
(Privately Owned)
IKSAN
PLANT
SIHWA
Head Quarter
VIETNAM
PLANT
Manufacturing
R&D
Sales
Admin
Finance
* NBD
Quality
Manufacturing
Management
Casting
Machining
Inspection
R&D 1
R&D 2
R&D 3
Production
Engineering
Tool
Building
Technical
Sales
*NBD
Sales
Management
Purchasing
HR
Accounting
**S.H.E
*New Business Development
**Safety, Health & Environment
Advanced development

## Slide 6: Ⅱ. Company Overview - Locations
Jeju
Busan
Incheon
Seoul
SIHWA Plant (HQ)
470 employees
34,014 Square meter / 32km from Seoul
(Machining, Washing, Assembly, Final Inspection, Packing, and Shipping)
MTV Plant
Completed on Oct12,2015
52,669 Square meter / 5 min from SIHWA
(Al Die casting, Trimming, Shot Blasting)
IKSAN Plant
122 employees
30,000 Square meter / 200km from Seoul
(Al Die casting, Trimming, Shot Blasting, Machining, Washing, Assembly, Final Inspection, Packing, and Shipping)
SIHWA & MTV
IKSAN
DAEYONG Plants

## Slide 7: Ⅱ. Company Overview - History
1983
DaeYong
Established
(Lead wire)
1992
Start Aluminum
Die Casting
(HDD to Samsung)
1993
Start Auto Parts
(Delphi)
1996
Vietnam Plant Established
2002
Start Biz with GM
2004
Start Biz with BorgWarner & NSK Steering
2006-2008
Start Biz with Allison, Kefico, Pierburg, & Valeo
2014
Start Biz with Hitachi USA
2015
Opened new MTV Plant (Sihwa)
2020
New DCMs
1,650-ton (2 sets), 2,500-ton (1 set) setup at MTV Plant
1999
Iksan Plant Established
Start Biz with Eaton & Molex
2022
Start Biz with SLPT &KyungShin Cable
2023
Start Biz with
Stellantis

## Slide 8: Ⅱ. Company Overview - Awards from Customers
2019
GM Supplier Quality Excellence Award
2018
GM Supplier Quality Excellence Award
2017
GM Supplier of the Year
GM Supplier Quality Excellence Award
2015
HITACHI Development Excellence Award
NSK Supplier of the Year
2012
EATON Supplier Excellence Award
2011
EATON Premier Supplier Award
2010
WABCO Supplier Excellence for Quality Award
2009
WABCO Premier Supplier Award
2007
BORGWARNER “Zero PPM” Accomplishment Award
2020
EATON Premier Supplier Award
GM Supplier of the Year
2021
GM Supplier of the Year
NSK President’s Club
2022
GM Supplier of the Year
2023
GM Supplier of the Year

## Slide 9: Ⅱ. Company Overview - Global Customers
EUROPE
〮 BorgWarner
〮 Eaton
〮 Pierburg
〮 Valeo
〮 ZF Wabco
THAILAND
〮 NSK Steering
KOREA
〮 GM Korea
〮 Aptiv Korea
〮 ZF Wabco Korea
〮 Kyungshin Cable
CHINA
〮 ZF Wabco China
AUSTRALIA
〮 Holden CCA
NORTH AMERICA
〮 GM
〮 Allison
〮 BorgWarner
〮 Continental
〮 Cosworth
〮 CSA
〮 Eaton
〮 Hitachi
〮 Molex
〮 NSK Steering
〮 Pierburg
SOUTH AMERICA
〮 GM Argentina
〮 GM Brazil
〮 ZF Wabco Brazil

## Slide 10
Steering
Transmission
Engine / Throttle Body /
Exhaust Gas Recirculation
Heat Exchanger
Steering Parts
Super Charger / Engine parts ●
EGR/ ETC ●
Air Compressor
EV Parts ●
Transmission Valve Body
Cam Carrier

## Slide 11
Ⅱ. Company Overview – ESG(Environment・Social・Governance)
ESG pledge signed around Feb,2022
Installed TMS equipment (chimney automation measurement monitoring equipment) on the melting facility dust collector.
Nitrogen oxide and dust discharge concentrations are being measured and analyzed every 10 seconds to keep them lower than the law regulations on atmospheric-related legal discharge concentrations.
For accurate measurement of TMS, specialized company do management for it, regularly conduct maintenance every month.
Realizing gender equality through the 'Women-Friendly Company Agreement' with Siheung City(Local Government) by actively hiring women and forming a women-friendly organizational culture.
M2030 Platform
DaeYong joined the platform in April 2024.
Low carbon manufacturing Program.

## Slide 12
High Quality Aluminum Die Casting and Machining, Complicated mold structures such as valve bodies
High vacuum casting system, weldable and improved mechanical property on casting parts (High Integrity Die Castings)
Focus on EV components such as Inverter Case / Motor Housing / Structural Parts
Invest further for larger Die casting machines(2,500 and 1,650ton) and related parts : LCE (lower crank extension), Oil pan, Engine Cover, Inverter case, EV motor case and Structural parts
Expand with additional factory in North America →US or Mexico
Additional Investment in automation
Support existing Engine and Transmission business
DaeYong Business Plan - Key Technologies and Future Strategy
Ⅱ. Company Overview - Commercial Overview of Company

## Slide 13: Ⅱ. Company Overview – Organizational Capabilities & Technical Capabilities
Program management and change management system
* Currently using UG, GM Tool kit - NX 2206 platform
* Parts Development Tools: 3D Printer, CT Scan, etc.
* Functional and Developmental Testing
- Porosity measurement equipment, and software that is the same as GM uses
- Sediment, particle control
Technical Capabilities

## Slide 14
Investment in Production technology and equipment as a % of sales in 2023: About 10.65%
 | Amount | Details
Sales | $ 100M | SIHWA+IKSAN plants
Investments | $ 10,650,000 | Production technology and Equipment: $10,650,000 (10.65% of sales)
Ⅱ. Company Overview – Continuous Improvement

## Slide 15: Ⅱ. Company Overview - Similar products currently producing
PN.: Part Name: | 12680230 CARRIER-CM/SHF (RH)
Material: | ALDC12
PPM: | 2023yr : 0ppm
Contracted period | Y2012 ~ 2025
PN.: Part Name: | 12694951 CARRIER-CM/SHF (LH)
Material: | ALDC12
PPM: | 2023yr : 0ppm
Contracted period | Y2017 ~ 2019
PN.: Part Name: | 12680229 CARRIER-CM/SHF (LH)
Material: | ALDC12
PPM: | 2023yr : 0ppm
Contracted period | Y2012 ~ 2025
PN.: Part Name: | 12694956 CARRIER-CM/SHF (RH)
Material: | ALDC12
PPM: | 2023yr : 0ppm
Contracted period | Y2017 ~ 2019
PN.: Part Name: | GD500883 CASE SUB ASSEMBLY
Material: | ALDC12
PPM: | 2023yr : 9ppm
Contracted period | Y2020 ~ 2026
PN.: Part Name: | GD500929 CASE SUB ASSEMBLY
Material: | ALDC12
PPM: | 2023yr : 0ppm
Contracted period | Y2020 ~ 2026

## Slide 16
Ⅱ. Company Overview – SSE Supplier Dashboard

## Slide 17: Ⅲ. Quality- Quality Metrics
  ▣ Sourceability Report Red-Yellow-Green chart status

## Slide 18: Ⅲ. Quality- Quality Metrics
  ▣ 9 – Panel Report
1) Nov. 8rd, 2023: Quality SPPS 165745
Missing material on PN#24246446.
2) Mar. 21th, 2024: Line Accumulation SPPS 179695
K-Hole Burr on PN#24047050.
3) Jun. 26th, 2024: Line Accumulation SPPS 190751
Porosity on PN#24047050.

## Slide 19: Ⅲ. Quality- Quality Metrics
  ▣ PPM internal & external per year for the last 5 year (Only for Gen2 Cam Carrier)
▣ GM Gen2 Cam Carrier Part Number: (LH Assy)12680229, (RH Assy)12680230
▣ External PPM based on Problem Case (Gen2 Cam Carrier) :
Y2020 Issue: SPPS 34758 / PN: 12680230 / Issue : Label Miss / Rejected Q’ty : 1 pallet (36pcs)

## Slide 20: Ⅲ. Quality- Quality Metrics
  ▣ PPM internal & external per year for the last 5 year (Only for Gen6 Cam Carrier)
▣ GM Gen2 Cam Carrier Part Number: (LH Assy)12694951, (RH Assy)12694956

## Slide 21
Ⅲ. Quality- Certificates
Safety
Environment
Quality
IATF 16949
(09/20/2022 ~ 09/19/2025)
ISO 45001
(12/19/2022 ~ 12/18/2025)
ISO 14001
(12/19/2022 ~ 12/18/2025)

## Slide 22: Ⅲ. Quality Data- PFMEA (Example)
EXAMPLE
22

## Slide 23: Ⅲ. Quality Data- Control Plan (Example)
EXAMPLE
23

## Slide 24: Ⅲ. Quality - Testing/Validation facilities and capabilities
Density Index
The amount of gas in molten metal to be measured and managed.
Spectrometer
The components of ingot and molten metal to be analyzed and managed.
Manufacturer : mk -GmbH
Model name : ALSP plus DT
Manufacturer : ALDCA
Model name : KA-383
Chemical Composition Analysis to be completed during the day/night
Day
Night
Day1
Night 1
Frequency: 2times/Shift
Day2
Night 2
Inspector name
Frequency: 1time/Shift

## Slide 25: Ⅲ. Quality - Testing/Validation facilities and capabilities
Component Cleanliness Cabinet
(To collect particle)
Particle Measurement Equipment
SAMPLE
Particle Measurement :
Size, Weight, Quantity
Manufacturer : PALL
Model name : Component Cleanliness Cabinet
Manufacturer : Sometech
Model name : SV-35 X 300 scale
Manufacturer : Motic
Model name : SMZ168
X 100 scale
Magnifier
Video
Microscope
system
Micro-
scope
Drying
machine
Micro-
balance

## Slide 26
Ⅲ. Quality - Testing/Validation facilities and capabilities
Universal Test Machine
SAMPLE
-Tensile Strength
-Yield Strength
-Elongation
-3 Point Break Strength
Rockwell
Hardness Tester
Brinell
Hardness Tester
Manufacturer : DaekyoungTech
Model name : DTU-900MH 10T
Manufacturer : Daekyoung Tech
Model name : DTR-200
Capacity : 150kgf
Manufacturer : KSTM
Model name : K-SHB-100
Capacity : 3,000kg

## Slide 27: Ⅲ. Quality - Testing/Validation facilities and capabilities
CT Scanner
CT Result Analysis
CT Scan Analysis Movie
For Inner porosity, Visualization analysis Movie
Before
After
3D
2D
SAMPLE
SAMPLE
X-ray Energy: 10kV~190kV
Detector Type : Flat Panel(DDA)
Detector Size : 400 x 400 mm
Sample Weight : 227 kg max.
Focal Spot Size : 500nm min.
-Porosity rate, Defect size, Reverse engineering rendering
-Satisfy ASTM-E2339, E2669, E2738, E2767 specifications
Manufacturer : NSI
Model name : X5000
Power : Max. 320W

## Slide 28: Ⅳ. Manufacturing Plan
20. Die Casting
& Trimming
*The concept can be changed during developing process.
10. Melting
Tilting Furnace
G.B.F
Toshiba Diecasting Machine (automation)
Trimming
Density Index
40. Machining
MTV
Machining Center Line
SIHWA
Machining Fixture
50. Washing
& Dry
Washing & Dry Machine
115. E.P.C
120. Packaging
& Shipping
Packing
Shipping
70. 2D Matrix
Visual Inspection
Shot blast Line (conveyor)
30. Shot Blast
90. Leak Test
2D Matrix
Leak Test
110. Final inspection
(Assembly check)
Final Inspection
80. Plug, Coil Assembly
BOLT SCREW, RETAINER BOLT, DOWEL PIN, ASSY ERRORPROOF VISION
60. Visual Inspection
100. Assembly
PLUG, COIL THREAD

## Slide 29: Ⅳ. Manufacturing Plan - Plant Layout (MTV)
*The concept can be changed during developing process.
Process Flow (MTV Plant)
1. Ingot Incoming
5. Incoming Inspection
10. Ingot Melting
15. Degassing (G.B.F)
20. Die Casting & Trimming
30. Shot Blasting
35. Moving (MTV → Sihwa plant)
MTV plant
A Zone
B Zone
C Zone
Ref. picture of MTV plant
MTV plant Layout (Zone “C”)
1
5
10
20
30
15
35
1) Aluminum ingot
5) Ingot inspection
Sihwa plant
20)Die Casting Machine : 1650 ton
15) Preheat & G.B.F Degassing equipment
10) Main Furnace – Ingot Melting
MTV plant Layout (Zone “A”)
30) Shot blast Equipment
Sihwa plant
MTV plant

## Slide 30: Ⅳ. Manufacturing Plan - Plant Layout (Sihwa)
*The concept can be changed during developing process.
70
Sihwa Plant Layout (3F)
60
110
80
2D Matrix
Leak test
Sihwa plant
Process Flow (Sihwa Plant)
35. Moving (MTV → Sihwa Plant)
40. Machining
50. Washing & Dry
60. Visual Inspection
70. 2D Matrix
80. Plug, Coil Assembly
90. Leak test
100. Dowel, Bolt, Retainer Assembly
110. Final Inspection
115. E.P.C
120. Packaging & Shipping
Ref. picture of Sihwa plant
A Zone
B Zone
Inspection (3F)
Warehouse (1F)
Warehouse
Visual Inspection
Final Inspection
E.P.C
Identify Area
40
50
Washing & Dry Machine
Machining Center
35
MTV plant
115
120
Packing
Sihwa Plant Layout (1F)
Sihwa plant
MTV plant
Dowel, Bolt, Retainer Assembly
90
Plug, Coil Assembly
100

## Slide 31: Ⅴ. Technical Data – Casting Concept
Mold Concept / 1 Cavity
*The concept can be changed during developing process.
Cavity
Biscuit
Runner
Overflow
● Die Casting Equipment
Equipment brand :SHIBAURA
Mold class: 1,650ton Die casting
Mold Material: S45C(Mold base), SKD61(Core)

## Slide 32: Ⅴ. Technical Data – Diecasting, Flow Analysis
*The concept can be changed during developing process.
Movie file – Click to play
Flow Pattern Analysis Result :
Analysis of the filling pattern shows that the filling is balanced overall.
Additional improvements could be made by changing the overflow location at the final filling point.
32
Movie file – Click to play
Cavity
Core
Analysis of Flow Pattern
Final filling point

## Slide 33: Ⅴ. Technical Data – Diecasting, Solidification
Movie file – Click to play
Solidification Analysis Movie
The patterns mean possibility to occur shrinkage, not porosity size.
A
A
Section A-A
Shrinkage Analysis Result :
Final solidification area is same as shrinkage
Shrinkage defect could be prevented as designing line cooling & spot cooling properly.
Solidification Analysis Result :
Final solidification area is relatively thick rib area.
Even though the final solidification area is casting shape(not machined surface and machined hole), it is located close to the machined areas.
Shrinkage defect could be prevented as designing line cooling & spot cooling properly.
*The concept can be changed during developing process.
B
B
Section B-B

## Slide 34: Ⅴ. Technical Data – Machining Concept
*The concept can be changed during developing process.
Equipment brand : Brother
Equipment model : W1000Xd1
Equipment size : 2,967 x 2,410 x 2,532 (mm)
Circular : 2 axes
Helical/conical : 3 axes（X,Y,Z)
(OP#10 Part holding View)
Machining OP.#10,#20 Fixture Concept
3 Clamps & 3 Pads (2 Pins)
(OP#20 Part holding View)
3 Clamps & 3 Pads (2 Pins)

## Slide 35: V. Technical Data – Machining Concept
*The concept can be changed during developing process.
#10 machining Process
Including Index turns to be original : 3 times / Turning operation is marked with green box
#10-4
Ø6.5 Inner Dia.(Datum Y)
#10-7
Ø8 Inner Dia. 14x
#10-5 Ø5 Inner Dia.
#10-6 Ø5.95 Inner Dia.
(Datum B.C)
#10-1,2(Roughening, Finishing)
#10-3 Brushing
Datum A(Face Milling)
#10-8
Ø8 Inner Dia. 4x
#11-1 Face Milling
#11-2,3 M12 Tap Drill, Tap Machining
#12-1 Ø8 Inner Dia. 2x
OP#11
Index turn
OP#12
Index turn
#10-9
Side Machining
(Gates Remove)

## Slide 36: V. Technical Data – Machining Concept
*The concept can be changed during developing process.
#20 machining Process
#20-1,2(Roughening, Finishing)
#20-3 Brushing (Datum F) (Face Milling)
#20-5
Ø11.85 Inner Dia. 2x
#20-4
Ø11.9 Inner Dia.

## Slide 37: Ⅵ. Manufacturing Plan – Automation Assembly Detail
1
11589108
(x12)
2
11562025 (x1)
3
DaeYong purchased components (No 1~8)
Appendix C BOM
4
5
6
7
8
BGH31732
(x1)
11588719
(x2)
11518792
(x16)
3525915
(x2)
55577568
(x1)
11503302
(x1)

## Slide 38: Ⅵ. Manufacturing Plan – Automation Assembly Detail
QTY: 12
1 |  | 11589108 | BOLT-HVY HEX ACORN FLG HD
2 |  | 11562025 | BOLT / SCREW
4 |  | 11588719 | BOLT / SCREW
5 | 7 | 11518792 | RETAINER – M6 BOLT
6 |  | 3525915 | PIN-DOWEL
QTY: 2
QTY: 2
QTY: 16
QTY: 1
3 |  | BGH31732 | BOLT / SCREW
QTY: 1

## Slide 39: Ⅵ. Manufacturing Plan – Automation Assembly Detail
7 |  | 55577568 | PLUG ASM-ENG OIL DRN
QTY: 1
8 |  | 11503302 | INSERT-METRIC COILED THREAD
QTY: 1

## Slide 40: Ⅵ. Manufacturing Plan – Automation Assembly Detail
*The concept can be changed during developing process.
Start
110.Assembly Check
missing ASM and
incorrect ASM
90. Leak Tesk
100. Dowel Pin press
101. Bolt Press fit
X2
70. 2D Matrix Marking
70
Asm check
81
SPEC : 10cc/min @ 70 ±3 kPa
X14
X2
X1
X1
80. Coil-Thread
X1
81. Plug
X1
100
101
110
80
90

## Slide 41: Ⅶ. Timing Plan – APQP Timing Chart

## Slide 42: Ⅶ. Timing Plan – Lead Time Detail - Gamma(PTB) Sample
No. | Description | Lead Time | Remark
1 | Tooling & Equipment | 16 weeks | Die-casting: In house Dimension check: By CMM The Lead time is from receipt of PO with 2D&3D. The date is negotiable with program timing. Quantity and lead time subject to change upon quotation update. Gamma(PTB) stage sample will be arranged based on 60 pcs according to the SOR appendix B. and bolt, retainer, coil, plug will be assembled manually.
2 | Tooling Verification | +8 weeks | 
3 | Gamma Production | +2 weeks | 
4 | Gamma Sample (shipping) | D+26 weeks | 
Gamma Lead Time
Gamma Tooling Lead Time Detail (all tooling can be used for production)
PAN ASM-UPR OIL 25206258 |  | 
Tooling | Lead Time | Quantity (set)
Die-Cast Mold | 16 weeks | 1
Trimming Jig | 16 weeks | 1
Machining Center (#10,20) | 16 weeks | 2
Leak Tester | 16 weeks | 1
Dowel Pin press | 16 weeks | 1
Gamma Tooling Total | 16 weeks | 6
*The concept can be changed during developing process.
(Reference)Appendix B Gamma MRD Schedule
: Gamma MRD : 15Jul25

## Slide 43: Ⅵ. Testing & Validation Plan – Appendix G (1)
*The concept can be changed during developing process.
SOR Appendix G – Validation Cross Reference Index
This List is from SOR Appendix G document, and the purpose is to check with GM
The reliability test items and testing numbers affect the piece price. It is necessary to discuss the items and quantities that can be simplified.
No. | Title | Evaluation Description | Notes | Type | Method | Qty | Duration Days | DYC Comment
1 | Mold Flow and Solidification Analysis | Meets Supplier Requirements | Cast Aluminum or Plastic Pan Only | D | Casting Simulation Analysis | When it is needed |  | AnyCasting Program used
2 | Drain Plug- Over Torque Testing at 20 and 100°C | Torque to Failure - Must break or strip drain plug first | Test with oil on the drain plug interface | PV | Visual Inspection | 3 set | 1 time/Day | 
3 | Drain Plug- Insertion/ Removal Testing (40 cycles) | Must not break pan or strip threads and pass leak test | Test with oil on the drain plug interface | PV | Visual Inspection | 3 set | 1 time/Day | 
4 | Threaded Plug - Over Torque Testing | >1.5 x Nominal Torque | If applicable | PV | Torque at Breaking (Nm) | 3 set | 1 time/Day | Check whether it is tested with Drain Plug
5 | Impact Resistance - Ball Drop Testing | 63.5 mm DIA, 1.05 kg Ball 2.0 m height Must not leak water (2.0 L) | Must test at least 4 locations including drain plug location. | PV | Visual Inspection | 1 set | 1 time/Day | 
6 | Hot Soak Test- Engine Oil at 150°C | Must not leak through casting (using florescent dye and black light) | Cast Aluminum Pan Only. Soak Pan filled with oil at 150°C for 24 hours. | PV | Visual Inspection | 3 set | 1 time/Day | 
7 | 100% Leak Test- Max Leak Rate Under Pressure | Cast Aluminum: 5 SCCM MAX @ 50 kPa |  | PV | Air Leak Rate Measurement (SCCM) | When it is needed |  | Leak test concept needs to be confirmed
Not required for production.
Only for the initial PPAP
Not required for production.
Only for the initial PPAP
Not required for production.
Only for the initial PPAP
Not required for production.
Only for the initial PPAP
Not required
100% check for production(Auto line)
GM Feedback applied after Tech review

## Slide 44: Ⅵ. Testing & Validation Plan – Appendix G (2)
*The concept can be changed during developing process.
SOR Appendix G – Validation Cross Reference Index
No. | Title | Evaluation Description | Notes | Type | Method | Qty | Duration Days | DYC Comment
8 | X-ray and Sectioning of Cast Parts | Meets Porosity Requirements | Cast Aluminum Pan Only | PV | Visual Inspection | 3 set | 1 time/Day | Need to check the cutting position
9 | Metallurgical Evaluation of Material | Meets Material Specification Requirements | Cast Aluminum Pan Only | PV | Visual Inspection | 3 set | 1 time/Day | 
10 | Visual Porosity Standards (Limit / Boundary Samples) | Meets Material Specification Requirements | Cast Aluminum Pan Only | PV | Visual Inspection | 1 set | 1 time/Day | 
11 | Water Dunk Testing- Audit | Cast Aluminum: No bubbles @ 100 kPa |  | PV | Visual Inspection | 1 set | 1 time/Day | 
12 | Cleanliness Measurement- Max Weight Only | Cast Aluminum Assembly: 15 mg MAX |  | PV | Measurement (mg) | 10 set | 1 time/Day* | a,Qty check required. b.Spec check c.Cleaness spec needs to be discussed
13 | RTV Adhesion Testing (after surface finish treatment) | GMUTS ≥ 8 (Standard: GMW17696) | Supplier must complete if applying RTV themselves (2 piece oil pans), otherwise this is done at the engine plant | PV | Visual Inspection | 1 set | 1 time/Week | Whether GM provides RTV for testing Whether Plasma Ashing Treatment is needed
This List is from SOR Appendix G document, and the purpose is to check with GM
The reliability test items and testing numbers affect the piece price. It is necessary to discuss the items and quantities that can be simplified.
Inspection for production
Inspection for production
Inspection for production
100% inspection for all parts prior to initial PPAP, not for production
Inspection for production
Inspection for production
Plasma treatment is done at GM facility
To do RTV, ultrasonic will be considered

## Slide 45: Ⅵ. Testing & Validation Plan – Testing Detail(1)
1.Mold Flow and
Solidification Analysis
Analysis of flow pattern & solidification
Quantity: Development stage, when it is needed
Frequency: Development stage, when it is needed
Any casting Program
Casting simulation
2. Drain Plug-
Over Torque Testing at 20 and 100°C
Heat the sample reaching to 100℃
Torque check
100℃
Room Temp 20℃ Sample preparation
20℃
Quantity: n=3 x 3 molds → 9set
Frequency: 1 time / day
*The concept can be changed during developing process.
Tapped holes & Plugs Damage check

## Slide 46: Ⅵ. Testing & Validation Plan – Testing Detail(2)
Assemble, disassemble
40 times repeat
3. Drain Plug-
Insertion/ Removal Testing (40 cycles)
Leak Test
Sample
Prepare
X1
Quantity: n=3 x 3 molds → 9set
Frequency: 1 time / day
4.Threaded Plug –
Over Torque Testing
Assembly Torque x 1.5times turning
To check Torque value
Rotate until the point of tapped hole and plug breakage
Quantity: n=3 x 3 molds → 9set
Frequency: 1 time / day
*The concept can be changed during developing process.
Tapped holes & Plugs Damage check
Tapped holes & Plugs Damage check
Plug Bolt (M12 : 1pc)
X1
Plug Bolt (M12 : 1pc)

## Slide 47: Ⅵ. Testing & Validation Plan – Testing Detail(3)
Check the impact location
Fill the sample with 2L of water and check for leaks
Assembled part preparation
Drop a Ø6.35 (1.05kg) steel ball into a 2m pipe and give a shock to parts.
Must test at least 4 points including drain plug location(Points needs to be discussed)
6. Hot Soak Test-
Engine Oil at 150°C
Fill engine oil + fluorescent dye in parts and heat it up to 150℃ in an oven
150℃
Check fluorescent dye penetration using a black light
Take out the sample and drain the engine oil
5. Impact Resistance - Ball Drop Testing
*The concept can be changed during developing process.
Quantity: n=1 x 3 molds → 3set
Frequency: 1 time / day

## Slide 48: Ⅵ. Testing & Validation Plan – Testing Detail(4)
11. Water Dunk Testing
Place the assembled part holding with the water dunk jig
Injecting air at 100 kPa pressure to check whether bubbles are generated
8. X-ray and Sectioning of Cast Parts
Quantity: n=3 x 3 molds → 9set
Frequency: 1 time / day
Cutting area needs to be discussed.
Internal porosity area & specifications need to be confirmed
Quantity: n=3 x 3 molds → 9set
Frequency: 1 time / day
*The concept can be changed during developing process.
SAMPLE
SAMPLE
SAMPLE
SAMPLE

## Slide 49: Ⅵ. Testing & Validation Plan – Testing Detail(5)
13. RTV Adhesion Testing
(after surface finish treatment)
Checking the adhesion grade after taking the RTV off
(Referring to GMW17696 standard)
Particles(Debris) Collection
Filter Dry
Check the weight difference before and after using the filter
Applying Provided RTV on
Surface of the sample
1mm x 1mm
height and width
Surface treated sample preparation
RTV Hardening (7 Days)
12. Cleanliness Measurement-
Max Weight Only
Assembled part sample
Preparation
Quantity: n=1 x 3 molds → 3set
Frequency: 1 time / Week
*The concept can be changed during developing process.
Quantity: n=10 x 3 molds → 30set
Frequency: 1 time / day

## Slide 50: Ⅷ. Engineering Design and Development - Open issue 1
Appendix_C :
#25206257 (machining) 2D : GMW5M-AL-C-D-Si10Cu2Fe-F
1. Aluminum Material Discussion
Material info
GMW5M-AL-C-D-Si10Cu2Fe-F is shown on 2D drawing note & SOR appendix C.
DaeYong’d like to propose changing ALDC12 or to add some additional comments like the box above.
Similar part’s material

## Slide 51: Ⅷ. Engineering Design and Development - Open issue 2
2. 2D Drawing(MCHG)
Discrepancy found between 2D dwg and 3D model
5501, 6601 – No 3D provided
501, 502 – No 3D provided
611 ~ 622 – No 3D provided

## Slide 52: Ⅷ. Engineering Design and Development - Open issue 3
3. 2D Drawing(ASSY)
Discrepancy found between 2D dwg and 3D model
“03” duplicate marking in 2D,
Components not shown in 3D model

## Slide 53: Ⅷ. Engineering Design and Development - Open issue 4
4. 2D Drawing(ASSY)
Discrepancy found between 2D dwg and SOR appendix C BOM List
#2025 qty
#9108 qty
#1732 qty
#7568, 3302 missing
3D model matches SOR appendix C
Appendix C BOM
2D Drawing BOM

## Slide 54: Ⅷ. Engineering Design and Development - Open issue 5
5. SHOT BLASTING
Shot blasting seems not allowed.
DaeYong would like to double check if it is okay to apply.

## Slide 55: Ⅷ. Engineering Design and Development - Open issue 6
6. 3D model proposal
Final solidification area, shape change proposal(mass removed)

## Slide 56: Ⅸ. Supply Chain Plan (Logistics, Packaging)
PAN ASM-UPR OIL 25206258 Packaging Concept
Packaging standard number :
1320B2 1320mm x 1140mm x 600mm
- STD pack : 24pcs / Pallet
Packing method could be discussed considering workability
*The concept can be changed during developing process.

## Slide 57: Ⅺ. Commercial review
Wrap up!